## Slide 1
PSV-7253-7254
Blocked Outlet Scenario

## Slide 2
Determine relief load
The Steam rated for this scenario reported by TOPSOE is 3700 and the normal flow is 1900 kg/h.
I do not know the reason why it is 3700 kg/h

## Slide 3
2.Calculate orifice area
Determine if it is in critical flow:
If so, then :

## Slide 6
Results
Note that the relieving temperature is obtained from TOPSOE EXCEL
T | 459 K | W | 3700 kg/h
Z | 0.92 | A | 7.92 cm2
M | 18.02 | A | 1.22 in2
C | 0.025 | Accumulation | 10%

## Slide 7
5.Use API-526 to determine the designation and the inlet and outlet sizing
Since it is less than 1.28inch, then J is selected. Also, by checking its rating and temperature limitation, 6Q8 is selected.

## Slide 9
Select proper PSV type by checking backpressure
According to licensor data, superimposed and build-up backpressure are max 1 barg. Since the backpressure is constant and it is discharged to atmosphere then a conventional type could be selected
superimposed | Build-up | Total
0 barg | 1 barg | 1 barg
0% | 22% | 22%

## Slide 10
Material Selection
Since it is Steam , A216 WCB could be used for its body

## Slide 11
Discussion
In PID TOPSOE has selected 2D3 but in LESER manual, 2J3 has been selected, which is according to my calculation