## Slide 1
PSV-5384-5386
Fire Scenario
wetted Surface

## Slide 2
PSV SIZING PROCEDURE FOR UNWETTED FIRE SCENARIO
1.Determine the scenario, using API-521
2.Calculate the relief load, using API-520 Part1
3.Calculate the orifice area, using API-520 Part1
4.Select proper PSV type by checking backpressure
5.Use API-526 to determine the designation and the inlet and outlet sizing
6.Use API-520 Part2 to detail its construction

## Slide 3
1.Determine the scenario, using API-521
Since it is K.N Drum and exposed to fire then a fire scenario is defined.
Parameters | Value | Parameters | Value
Diameter | 3.9m | M | 32
Height | 4.555 m | Set Pressure | 19 barg
Fluid | Methanol | Relieving Pressure | 23.99 bara
Z | 0.8 | Accumulation | 0.21
Cp/Cv | 1.1 | Material | CS

## Slide 4
2.Calculate the relief load, using API-520 Part1
Where adequate drainage and firefighting equipment do not exist, Equation (8) should be used

## Slide 5
Calculation
Parameters | Value
Aw | 72.4 m2
C2 | 70900
F | 1
λ | 832 kj/kg
Relief load | 10269 kg/h

## Slide 6
3.Calculate orifice area
Determine if it is in critical flow:
If so, then :

## Slide 9
5.Use API-526 to determine the designation and the inlet and outlet sizing
Since it is more than 0.78 inch then J is selected. Also, by checking its rating and temperature
limitation, 2J3 is selected. But Topsoe has selected 2H3 in site .

## Slide 11
Select proper PSV type by checking backpressure
According to licensor data, superimposed and build-up backpressure are max 21barg. Even though selecting Conventional type is not recommended, Conventional type has been selected by LESER.
superimposed | Build-up | Total
1.5 barg | 13 barg | 14.5 barg
8% | 68% | 76%

## Slide 12
Material Selection
Since it is methanol then A-216 WCB is selected for its body

## Slide 13
Discussion
The relief load calculated by TOPSOE greatly differs by my calculation and that of TCC which is due to change in X-5001 height later in project.
Another thing is that by my calculation 2J3 is suitable for this but TOPSOE has selected 2H3.
TCC Calculation