## Slide 1
Rupture Disk
Rupture disk devices are non-reclosing PRDs used to protect vessels, piping, and other
pressure-containing components from excessive pressure and/or vacuum. Rupture disks are used in
single and multiple relief device installations. They are also used as redundant PRDs.
With no moving parts, rupture disks are simple, reliable, and faster acting than other PRDs.
Rupture disks react quickly enough to relieve some types of pressure spikes. Because of their light
weight, rupture disks can be made from high alloy and corrosion resistant materials that are not practical
in PRVs.
Rupture disks can be specified for systems with vapor (gas) or liquid pressure-relief
requirements. Also, rupture disk designs are available for highly viscous fluids. The use of rupture disk
devices in liquid service should be carefully evaluated to ensure that the design of the disk is suitable for
liquid service. The user should consult the manufacturer for information regarding liquid service
applications.

## Slide 2
Rupture disk devices often have different opening characteristics as a function of the fluid state
against the disk at the time of bursting. To account for the resulting differences in the resistance to flow,
certified Kr values are stated in terms of Krg (gas), Krl (liquid), or Krgl (gas or liquid). In application, use the
following guidelines.
1.When the fluid initiating rupture (in contact with rupture disk) is compressible, rupture disks rated with
Krg or Krgl should be used.
2.When the fluid initiating rupture (in contact with rupture disk) is incompressible, rupture disks rated
with Krl or Krgl should be used.
The rupture disk is also a temperature-sensitive device. Burst pressures can vary significantly
with the temperature of the rupture disk device. This temperature may be different from the normal fluid
operating temperature. As the temperature at the disk increases, the burst pressure usually decreases.
Since the effect of temperature depends on the rupture disk design and material, the manufacturer should
be consulted for specific applications. For these reasons, the rupture disk shall be specified at the
pressure and temperature the disk is expected to burst.

## Slide 3
Application of Rupture Disks
Rupture disks can be used in any application requiring overpressure protection where a non-reclosing
device is suitable. This includes single, multiple, and fire applications as specified in UG-134 of the ASME
Code.
Rupture Disk Device at the Inlet of a Pressure-relief Valve
Rupture disks are used upstream of PRVs to seal the system to meet emissions standards, to
provide corrosion protection for the valve, and to reduce valve maintenance.
When a rupture disk device is installed at the inlet of a PRV, the devices are considered to be
close coupled, and the specified burst pressure and set pressure should be the same nominal value.
When installed in liquid service, it is especially important for the disk and valve to be close coupled to
reduce shock loading on the valve
The space between the rupture disk and the PRV shall have a free vent, pressure gauge,
trycock, or suitable telltale indicator as required in UG-127 of the ASME Code. Users
are warned that a rupture disk will not burst in tolerance if backpressure builds up in a nonvented space
between the disk and the PRV, which will occur should leakage develop in the rupture disk due to
corrosion or other cause (

## Slide 4
Rupture Disk Device at the Outlet of a Pressure-relief Valve
A rupture disk device may be installed on the outlet of a PRV to protect the valve from atmospheric or
downstream fluids. Consideration should be given to the valve design so that it will open at its proper
pressure setting regardless of any backpressure that may accumulate between the valve and rupture
disk.
Types of Rupture Disks
There are three major rupture disk types
1. Forward-acting, tension-loaded
2. Reverse-acting, compression-loaded;
3. Graphite, shear-loaded.

## Slide 5
Forward-acting Solid Metal Rupture Disks
A forward-acting rupture disk is a formed (domed), solid metal disk designed to burst at a rated pressure
applied to the concave side (see Figure 21). This rupture disk typically has an angular seat design and
provides a satisfactory service life when operating pressures are up to 70 % of the marked burst pressure
of the disk (70 % operating ratio). Consult the manufacturer for the actual recommended operating ratio
for the specific disk under consideration. If vacuum or backpressure conditions are present, the disk can
be furnished with a support to prevent reverse flexing. These disks have a random opening pattern and
are considered fragmenting designs that are not suitable for installation upstream of a PRV

## Slide 7
Forward-acting Scored Rupture Disks
The scored forward-acting rupture disk is a formed (domed) disk designed to burst along scored lines
at a rated pressure applied to the concave side (see Figure 22). Some designs provide satisfactory
service life when operating pressures are up to 85 % to 90 % of the marked burst pressure of the disk
(85 % to 90 % operating ratio). Most designs withstand vacuum conditions without a vacuum
support. If backpressure conditions are present, the disk can be furnished with a support to prevent
reverse flexing. Because the score lines control the opening pattern, this type of disk can be manufactured to be
nonfragmenting and is acceptable for installation upstream of a PRV. The scored,
forward-acting rupture disk is manufactured from thicker material than nonscored designs with the
same burst pressure, and it provides additional resistance to mechanical damage.

## Slide 9
Forward-acting Scored Rupture Disks
A forward-acting composite rupture disk is a flat or domed multipiece construction disk (see
Figure 23). The domed composite rupture disk is designed to burst at a rated pressure applied to the
concave side. The flat composite rupture disk may be designed to burst at a rated pressure in either or
both directions. Some designs are nonfragmenting and acceptable for use upstream of a PRV. A flat composite
rupture disk is available for the protection of low-pressure vessels or the isolation of equipment such as exhaust
headers or the outlet side of a PRV. This disk usually comes complete with gaskets and is designed to be installed
between companion flanges rather than within a specific rupture disk holder. Flat composite rupture disks
generally provide satisfactory service life when operating pressures are 50 % or less of the marked burst pressure
(50 % operating ratio). The slits and tabs in the top section provide a predetermined opening pattern for the
rupture disk. If vacuum or backpressure conditions are present, composite disks can be furnished with a support
to prevent reverse flexing (see Figure 23). A domed, composite rupture disk generally provides satisfactory
service life when the operating pressure is 80 % or less of the marked burst pressure (80 % operating ratio).

## Slide 10
A flat composite rupture disk is available for the protection of low-pressure vessels or the
isolation of equipment such as exhaust headers or the outlet side of a PRV. This disk usually comes
complete with gaskets and is designed to be installed between companion flanges rather than within a
specific rupture disk holder. Flat composite rupture disks generally provide satisfactory service life when
operating pressures are 50 % or less of the marked burst pressure (50 % operating ratio).
Reverse-acting Rupture Disks
A reverse-acting rupture disk typically is a formed (domed) solid metal disk designed to reverse
and burst at a rated pressure applied on the convex side. Reverse-acting rupture disks are designed to
open by such methods as shear knife blades, tooth rings, or scored lines Reverse-acting rupture disks may be
manufactured as nonfragmenting and are suitable for installation upstream of PRVs. These disks provide
satisfactory service life when operating pressures are 90 % or less of marked burst pressure (90 % operating
ratio). Some types of reverse-buckling disks are designed to be exposed to pressures up to 95 % of the marked
burst pressure. Consult the manufacturer for the actual recommended operating ratio for the specific disk under
consideration. Because a reverse acting rupture disk is operated with pressure applied on the convex side,
thicker disk materials may be used, thereby lessening the effects of corrosion, eliminating the need for vacuum
support, and providing longer service life under pressure/vacuum cycling conditions and pressure fluctuations

## Slide 12
Graphite Rupture Disks
Graphite rupture disks are typically machined from a bar of fine graphite that has been
impregnated with a sealing compound to seal the porosity of the graphite matrix (see Figure 26). The disk
operates on a pressure differential across the center diaphragm or web portion of the disk. Graphite
rupture disks provide a satisfactory service life when operating pressures are up to 80 % of the marked
burst pressure (80 % operating ratio) and can be used in both liquid and vapor service.
If vacuum or backpressure conditions are present, the disk can be furnished with a support to
prevent reverse flexing. These disks have a random opening pattern and are considered fragmenting
designs that are not suitable for installation upstream of a PRV. A metallic ring called armoring is often
added to the outside diameter of the disk to help support uneven piping loads and minimize the potential
for cracking of the outer graphite ring and blowout of process fluid.

## Slide 14
Rupture Disk Selection
the user is cautioned to make sure that the upper limit of the manufacturing design range does not exceed the MAWP
of the equipment being protected.

## Slide 18
Selection Procedure

## Slide 19
Sizing Procedure