## Slide 1
Vertical Vessel
With Mesh Mist Eliminator
D-3001
Design and Principles

## Slide 2
Operating Parameters
Description
The objective of this vessel is to separate liquid particle from the gas . The vessel is located at the
suction of a centrifugal compressor so that maximum droplet size contained in gas stream to
compressor should be max 10 micron.

## Slide 3
Design Procedure
1. Select proper Orientation
2. Select and Size proper Inlet Device, Inlet and Outlet ID
3.Calculate Vessel Diameter
4. Calculate Vessel Height
5.Select and Size Manholes, Vent, Drain, Vortex Breaker
6. Select a well-designed mist eliminator pad

## Slide 4
1st Step: Select proper orientation
Since the application is gas dominant a vertical vessel is selected .
Due to its being at the suction of the compressor , a mesh mist eliminator should be installed.

## Slide 6
2nd Step: Select and Size proper Inlet Device
Half Pipe has proven itself to be not only effective in large capacities but cost-effective as well and in
many application is preferred to Diffuser whose performance is superior but too costly.

## Slide 7
It is also necessary to maintain the inlet velocity head, J, within proper limits for the selected inlet
device to insure good gas distribution and minimum liquid shattering.
Where,
J = (ρV²) .
The maximum mixed phase velocity head range used in the industry guidelines varies for the different
inlet devices. Some typical maximums are:
•6000-9000 max. typ, up to 15 000 max kg/m s2 for diffuser distributor
•975-2250 max kg/m.s2 for no inlet distributor
•1500-3750 max kg/m.s2 for inlet half pipe or elbow distributor
•1500-3750 max kg/m.s2 for v-baffle or other simple inlet diverter designs
In addition, some users limit the inlet vapor phase velocity to 9 m/s or 18 m/s. The velocity should
always be below the erosion velocity for the service.

## Slide 8
In order to calculate head velocity , at first, we need to perform the followings:
1. Estimation of inlet nozzle ID; Consider inlet pipe ID near the vessel as first and best estimation.
2. Calculate ρmixture and subsequently Vmixture
3. Calculate J by multiplying ρmixture (Vmixture)^2 and compare it with the last-page criterion.
The licensor has divided upstream inlet piping 42’ into 3 inlet piping which is a good course of action to
take since the load of inlet to this separator drum is so high . Therefore in order to have the same inlet
area , 42’ is divided by 3^0.5 and the result would be 24’.
Parameter | Value | Value | Unit
Estimated ID | 42 | 40 | inch
Nozzle Area | 0.89 | 0.81 | m2
ρmixture | 44.37 | 44.37 | kg/m3
Vmixture | 7.88 | 8.69 | m/s
J | 2757 | 3351 | kg/m.s2
Criterion | 3750 | 3750 | kg/m.s2

## Slide 9
So, both 24 and 23 inch are accepted but it is recommended that inlet piping diameter match the
velocity requirement of the inlet to the separator 10 pipe diameters upstream of the separator to
provide a flow regime which is fully developed before entering the separator. Thus, 24 inch is accepted.

## Slide 11
Vapor Outlet Section
The sizing of the vapor outlet nozzle should be such that given the above placement of the mesh pad,
the velocity is not high enough to cause channeling of the gas through the mesh pad. The nozzle outlet
size is typically based on the lesser of that required for piping pressure drop, or a maximum velocity
head criteria. Typical ranges for the maximum velocity head allowed for the vapor outlet are 4500–
5400 kg/m • s2. In addition some users limit the absolute velocity to 18 m/s. The pipe size can be
decreased to the appropriate size based on pressure drop considerations, 5-10 pipe diameters
downstream of the separator, as required.
Parameter | Value | Value | Unit
Estimated ID | 34 | 30 | inch
Area | 0.585 | 0.45 | m2
Vg | 11.87 | 15.25 | m/s
ρVg2 | 4950 | 8165 | Kg/m.s2
Criterion | 5400 | 5400 | Kg/m.s2

## Slide 12
Note
The licensor has chosen 30 inch but it has exceeded conventional criteria. By the way upper limit of this
criteria has been selected for outlet nozzle sizing due to high volume of gas going out of the vessel.

## Slide 13
Liquid Outlet Nozzle
Since it is going to be discharged to another vessel , the maximum velocity should be 3 m/s and the
average velocity should be 2 m/s.
It sounds both 8 and 10 inch are acceptable but I prefer 10 inch thanks to its being near 2 m/s as
selected average velocity . The licensor has chosen 10 inch as the Outlet nozzle size .
Parameter | Value | Value | Unit
Estimated ID | 8 | 10 | inch
Area | 0.032 | 0.05 | m2
Vl | 2.79 | 1.78 | m/s
Criterion | Max 3 | Max 3 | m/s

## Slide 14
3rd Step: Calculate Vessel Diameter
Each and every licensor and company has developed a design basis procedure for sizing vessels. In this
Article , a GPSA-based method, Foster-Wheeler-based method and the Licensor method will be
explored.

## Slide 15
GPSA
1. Use the following equation and next-page K-values to calculate terminal velocity

## Slide 16
De-rating factor to K-value for pressure Typical Saunders Brown K values for mist
eliminator devices

## Slide 17
According to Saunders-Brown K-value , thanks to the fact that a vertical vessel with demister pad has
been chosen, a K value of 0.11 is selected. Furthermore, since the performance of demister pad varies
According to operating pressure, the selected K should be de-rated in accord with last-page Table.
Kde-rated = 0.11
Parameter | Value | Unit
ρl | 757 | kg/m3
ρv | 35.1 | kg/m3
Kselected | 0.0825 | 
Ug | 0.37 | m/s
Qg | 6.95 | m3/s
ID | 4866 | mm
Required-ID | 5016 | mm
Selected-ID | 5000 | mm

## Slide 18
Notes
For ID calculation , the following equation has been utilized.
Also since the demister pad is mounted on a support ring , then 150 mm or 6 inch is added to calculated
ID, which results in 4866 + 150 = 5016 mm, which is regarded as the required ID. The selected ID
would be rounded to 5000 mm.
The selected ID is in great harmony with the Licensor selected ID, which is 4900 mm.

## Slide 19
Foster-Wheeler
The basis of sizing is the critical velocity Vc (m/s)
The maximum gas velocity is KVc
K is a coefficient depending on the service, and the use or the absence of wire mesh.
Recommended K values are given hereafter for different services.
If a vane pack internal is used, the recommended K value is 3.3.

## Slide 20
Parameter | Value | Unit
ρl | 757 | kg/m3
ρv | 35.1 | kg/m3
Kselected | 1.7 | 
Vc | 0.25 | m/s
Vmax | 0.425 | 
Qg | 6.95 | m3/s
ID | 4563 | mm
Required-ID | 4713 | mm
Selected-ID | 4700 | mm

## Slide 21
4th Step: Height Calculation
Each and every licensor and company has developed a design basis procedure for sizing vessels. In this
Article , a GPSA-based method, Foster-Wheeler-based method and the Licensor method will be
explored.

## Slide 22
GPSA

## Slide 23
Retention/Surge Time

## Slide 24
Height Elements | GPSA | LICENSOR | Unit
H1 | 450 | - | mm
H2 | 1375 | 1300 | mm
H3 | 1250 | 1170 | mm
H4 | 610 | 610 | mm
H5 | 2500 | 2650 | mm
H6 | 150 | 150 | mm
H7 | 150 | 150 | mm
HT | 6485 | 6100 | mm

## Slide 25
Calculation, Explanation, and Discussion
H1 mostly depends on instrument mount position and the number of instrument devices used . The
Licensor for most of his vertical vessel has selected 500 mm in accord with his FCS and ESD Control
System, whereas in GPSA 450 mm is selected as the basis.
H2 is a function of retention time . It seems from the back-calculation that the licensor has selected 5
minutes for retention time . Likewise, in GPSA a retention time of 2-5 minutes has been selected for
Flash drums. The licensor general retention time table is given in next-page
H3 in GPSA for Half Open pipes is 0.25D and has been the basis for calculation.
H4 is the size of inlet Half Open pipe which is the same size of upstream pipe for both licensor and
GPSA.
H5 in GPSA for Half Open pipes is 0. 5D and has been the basis for calculation.
H6 is the demister pad thickness which is 150 mm for both licensor and GPSA.
H7 in GPSA is minimum 150 mm but in other sketch in GPSA there is a formula for X4 which connects
the upper part of demister pad to outlet nozzle which can not be used for comparison here.

## Slide 26
Note
The licensor has selected a spherical head for both top and bottom of the vessel, which is well-designed.
The reason why the licensor has selected such head type is mainly due to high liquid flow and by
selecting spherical head type it could create hold-up space for retention time purposes , which helps to
greatly reduce vessel height .

## Slide 27
Retention Time provided by the licensor

## Slide 29
Foster-Wheeler

## Slide 30
Height Elements | FW | LICENSOR | Unit
H1 | 300 | 500 | mm
H2 | 575 | 500 | mm
H3 | - | 600 | mm
H4 | 865 | 865 | mm
H5 | - | 1700 | mm
H6 | 150 | 150 | mm
H7 | - | 525 | mm
HT | - | 4825 | mm

## Slide 31
Manholes
Foster-Wheeler
Size of manholes
For vessel diameter < 1000 mm
Flanged vessel shall be considered if equipment contains internals
Otherwise, size of manholes = 18”
For vessel diameter ≥ 1000 mm
Toxic service size of manholes = 24”
Non-toxic service size of manholes = 20”
(or up to 24” if internals need to be removable through
manhole.)

## Slide 32
Drain and Vents
The drain of the vessel shall always be at the lowest point of a vessel. For vertical vessels they
shall be connected to the bottom outlet line at the low point. For horizontal vessels the drain point
shall be directly on the bottom of the drum at the lowest point ensured through vessel slope (1:100).

## Slide 33
Licensor Criteria

## Slide 34
Comparison
The size of manhole for both licensor and FW is 24’.
There is no need to have Vent on this drum since there is a control valve to flare system and if
purging is required then by use of these means the task could be performed.
The drain valve sized by licensor is 2’ and but by Foster-Wheeler is 4’. According to licensor data a
drain valve with 3’ sizing should have been selected
Parameter | FW | Licensor
Manhole | 20-24 | 24
Vent | 3 | -
Drain | 4 | 2
Vortex Breaker | Yes | Yes

## Slide 35
6th Step : Select a well-designed Mist Eliminator pad
Using KG TOWER

## Slide 36
Put operating data as input like below

## Slide 37
In Koch-Glitsch products there are two types of demister pads :
Traditional demister pads
High efficiency demister pads

## Slide 38
All types will be selected and the results are compared

## Slide 40
High Efficiency Demister Pad