## Slide 1
Vertical Vessel
With Mesh Mist Eliminator
D-6001
Design and Principles

## Slide 2
Operating Parameters
Description
The objective of this vessel is to separate liquid particle from the gas . The vessel is located at the
Inlet of reforming reactors so that maximum droplet size contained in gas stream to
the section should be max 10 micron.

## Slide 3
Design Procedure
1. Select proper Orientation
2. Select and Size proper Inlet Device, Inlet and Outlet ID
3.Calculate Vessel Diameter
4. Calculate Vessel Height
5.Select and Size Manholes, Vent, Drain, Vortex Breaker
6. Select a well-designed mist eliminator pad

## Slide 4
1st Step: Select proper orientation
Since the application is gas dominant a vertical vessel is selected .
Due to its being at the inlet of reforming reactors, a mesh mist eliminator should be installed.

## Slide 6
2nd Step: Select and Size proper Inlet Device
Half Pipe has proven itself to be not only effective in large capacities but cost-effective as well and in
many application is preferred to Diffuser whose performance is superior but too costly.

## Slide 7
It is also necessary to maintain the inlet velocity head, J, within proper limits for the selected inlet
device to insure good gas distribution and minimum liquid shattering.
Where,
J = (ρV²) .
The maximum mixed phase velocity head range used in the industry guidelines varies for the different
inlet devices. Some typical maximums are:
•6000-9000 max. typ, up to 15 000 max kg/m s2 for diffuser distributor
•975-2250 max kg/m.s2 for no inlet distributor
•1500-3750 max kg/m.s2 for inlet half pipe or elbow distributor
•1500-3750 max kg/m.s2 for v-baffle or other simple inlet diverter designs
In addition, some users limit the inlet vapor phase velocity to 9 m/s or 18 m/s. The velocity should
always be below the erosion velocity for the service.

## Slide 8
In order to calculate head velocity , at first, we need to perform the followings:
1. Estimation of inlet nozzle ID; Consider inlet pipe ID near the vessel as first and best estimation.
2. Calculate ρmixture and subsequently Vmixture
3. Calculate J by multiplying ρmixture (Vmixture)^2 and compare it with the last-page criterion.
So, the inlet device sizing should at least be 30 inch to meet the momentum requirement but the
licensor has taken into account recommended practice that inlet piping diameter match the
velocity requirement of the inlet to the separator 10 pipe diameters upstream of the separator to
provide a flow regime which is fully developed before entering the separator. Thus 28 inch has been
selected.
Parameter | Value | Value | Value | Unit
Estimated ID | 28 | 30 | 32 | inch
Nozzle Area | 0.39 | 0.45 | 0.51 | m2
ρmixture | 37.9 | 37.9 | 37.9 | kg/m3
Vmixture | 11.47 | 10 | 8.78 | m/s
J | 5003 | 3796 | 2932 | kg/m.s2
Criterion | 3750 | 3750 | 3750 | kg/m.s2

## Slide 10
Vapor Outlet Section
The sizing of the vapor outlet nozzle should be such that given the above placement of the mesh pad,
the velocity is not high enough to cause channeling of the gas through the mesh pad. The nozzle outlet
size is typically based on the lesser of that required for piping pressure drop, or a maximum velocity
head criteria. Typical ranges for the maximum velocity head allowed for the vapor outlet are 4500–
5400 kg/m • s2. In addition some users limit the absolute velocity to 18 m/s. The pipe size can be
decreased to the appropriate size based on pressure drop considerations, 5-10 pipe diameters
downstream of the separator, as required. 24 inch is selected.
Parameter | Value | Value | Value | Unit
Estimated ID | 22 | 24 | 28 | inch
Area | 0.24 | 0.29 | 0.39 | m2
Vg | 18.2 | 15.3 | 11.23 | m/s
ρVg2 | 6890 | 4865 | 2626 | Kg/m.s2
Criterion | 5400 | 5400 | 5400 | Kg/m.s2

## Slide 11
Liquid Outlet Nozzle
Many users limit the liquid outlet nozzle velocity based on pump suction line criteria
It sounds both 12 and 14 inch are acceptable but the licensor has chosen 16 inch as the ultimate sizing
for liquid outlet.
Parameter | Value | Value | Value | Unit
Estimated ID | 12 | 14 | 16 | inch
Area | 0.072 | 0.099 | 0.12 | m2
Vl | 1.32 | 0.97 | 0.74 | m/s
Criterion | Max 1.5 | Max 1.5 | Max 1.5 | m/s

## Slide 12
3rd Step: Calculate Vessel Diameter
Each and every licensor and company has developed a design basis procedure for sizing vessels. In this
Article , a GPSA-based method, Foster-Wheeler-based method and the Licensor method will be
explored.

## Slide 13
GPSA
1. Use the following equation and next-page K-values to calculate terminal velocity

## Slide 14
De-rating factor to K-value for pressure Typical Saunders Brown K values for mist
eliminator devices

## Slide 15
According to Saunders-Brown K-value , thanks to the fact that a vertical vessel with demister pad has
been chosen, a K value of 0.11 is selected. Furthermore, since the performance of demister pad varies
According to operating pressure, the selected K should be de-rated in accord with last-page Table.
Kde-rated = 0.11
Parameter | Value | Unit
ρl | 832 | kg/m3
ρv | 20.8 | kg/m3
Kselected | 0.088 | 
Ug | 0.54 | m/s
Qg | 4.46 | m3/s
ID | 3216 | mm
Required-ID | 3366 | mm
Selected-ID | 3400 | mm

## Slide 16
Notes
For ID calculation , the following equation has been utilized.
Also since the demister pad is mounted on a support ring , then 150 mm or 6 inch is added to calculated
ID, which results in 3216 + 150 = 3366 mm, which is regarded as the required ID. The selected ID
would be rounded to 3400 mm.
The selected ID is in complete harmony with the Licensor selected ID, which is 3400 mm.

## Slide 17
Foster-Wheeler
The basis of sizing is the critical velocity Vc (m/s)
The maximum gas velocity is KVc
K is a coefficient depending on the service, and the use or the absence of wire mesh.
Recommended K values are given hereafter for different services.
If a vane pack internal is used, the recommended K value is 3.3.

## Slide 18
Parameter | Value | Unit
ρl | 832 | kg/m3
ρv | 20.8 | kg/m3
Kselected | 1.7 | 
Vc | 0.31 | m/s
Vmax | 0.53 | 
Qg | 4.46 | m3/s
ID | 3271 | mm
Required-ID | 3421 | mm
Selected-ID | 3400 | mm

## Slide 19
4th Step: Height Calculation
Each and every licensor and company has developed a design basis procedure for sizing vessels. In this
Article , a GPSA-based method, Foster-Wheeler-based method and the Licensor method will be
explored.

## Slide 20
GPSA

## Slide 21
Retention/Surge Time

## Slide 22
Height Elements | GPSA | LICENSOR | Unit
H1 | 450 | 500 | mm
H2 | 6300 | 5625 | mm
H3 | 850 | 670 | mm
H4 | 720 | 720 | mm
H5 | 1700+2400 | 2695+2400 | mm
H6 | 150 | 150 | mm
H7 | 150 | 150 | mm
HT | 12720 | 12400 | mm

## Slide 23
Calculation, Explanation, and Discussion
H1 mostly depends on instrument mount position and the number of instrument devices used . The
Licensor for most of his vertical vessel has selected 500 mm in accord with his FCS and ESD Control
System, whereas in GPSA 450 mm is selected as the basis.
H2 is a function of retention time . It seems from the back-calculation that the licensor has selected 5
minutes for retention time . Likewise, in GPSA a retention time of 2-5 minutes has been selected for
Flash drums. The licensor general retention time table is given in next-page
H3 in GPSA for Half Open pipes is 0.25D and has been the basis for calculation.
H4 is the size of inlet Half Open pipe which is the same size of upstream pipe for both licensor and
GPSA.
H5 in GPSA for Half Open pipes is 0. 5D and has been the basis for calculation. Since we have 5 tray
For sodium removal purposes then 4 × 600 = 2400 mm is added to H5.
H6 is the demister pad thickness which is 150 mm for both licensor and GPSA.
H7 in GPSA is minimum 150 mm but in other sketch in GPSA there is a formula for X4 which connects
the upper part of demister pad to outlet nozzle which can not be used for comparison here.

## Slide 24
Retention Time provided by the licensor

## Slide 25
Note :
ID and number of passes estimated only. ID must not be lowered as separator function is design
giving . Final dimensions number of passes to be confirmed by tray vendor.

## Slide 27
Foster-Wheeler

## Slide 28
Height Elements | FW | LICENSOR | Unit
H1 | 300 | 500 | mm
H2 | 6300 | 500 | mm
H3 | - | 600 | mm
H4 | 720 | 865 | mm
H5 | - | 1700 | mm
H6 | 150 | 150 | mm
H7 | - | 525 | mm
HT | - | 4825 | mm

## Slide 29
Manholes
Foster-Wheeler
Size of manholes
For vessel diameter < 1000 mm
Flanged vessel shall be considered if equipment contains internals
Otherwise, size of manholes = 18”
For vessel diameter ≥ 1000 mm
Toxic service size of manholes = 24”
Non-toxic service size of manholes = 20”
(or up to 24” if internals need to be removable through
manhole.)

## Slide 30
Drain and Vents
The drain of the vessel shall always be at the lowest point of a vessel. For vertical vessels they
shall be connected to the bottom outlet line at the low point. For horizontal vessels the drain point
shall be directly on the bottom of the drum at the lowest point ensured through vessel slope (1:100).

## Slide 31
Licensor Criteria

## Slide 32
Comparison
The size of manhole for both licensor and FW is 24’.
There is no need to have Vent on this drum since there is a control valve to flare system and if
purging is required then by use of these means the task could be performed.
The drain valve sized by licensor is 2’and but by Foster-Wheeler is 3’ and in site 3’.
Parameter | FW | Licensor
Manhole | 20-24 | 24
Vent | 2 | 2
Drain | 3 | 2
Vortex Breaker | Yes | Yes

## Slide 33
6th Step : Select a well-designed Mist Eliminator pad
Using KG TOWER

## Slide 34
Put operating data as input like below

## Slide 35
In Koch-Glitsch products there are two types of demister pads :
Traditional demister pads
High efficiency demister pads

## Slide 36
All types will be selected and the results are compared

## Slide 39
The best options that could be selected seem to be York mesh 172 , 709 and 708 since they have higher
max K value and lowest dp .